## Slide 1: Chapter 2: Image processing and computer vision
Camera models and parameters
Notes: In this chapter we will learn the mathematical model of a computer and how to use the parameters involved.

## Slide 2: Learn these in this chapter
Mathematical model of a camera
Intrinsic (static) parameters of a camera (Mint3x3)
  Focal length (f) for fixed focal length, non-zoomed cameras
  Image center (Ox,Oy)
  Pixel width/height (Sx,Sy)
Extrinsic (dynamic) parameters of a camera (Mext3x4)
  Rotation (R) and Translation (T) of a camera
  Characteristics of R and T
Image formation and projection matrix P3x4

## Slide 3: Motivations
Digital cameras are everywhere.
Develop applications for cameras.
Help to choose a good camera.
Notes: Before we learn how to use a camera for various applications we need to know the parameters and their characteristics.

## Slide 4: 3D to 2D projection
Perspective model
u=F*X/Z
v=F*Y/Z
F
Z
Y
v
World
center
F
Thin lens
or a pin hole
Virtual
Screen
or CCD
https://en.wikipedia.org/wiki/Charge-coupled_device
sensor
Real
Screen
Or
CCD
sensor
Pinhole
Camera
http://upload.wikimedia.org/wikipedia/en/8/81/Pinhole-camera.png
v
Notes: From your secondary school physics, you probably have learn this mode, if you place a lens in front of a screen you get the inverted image. A pin hoe camera and a thin lens camera are similar. The image is a 2D projection of the 3D world.

## Slide 5: Perspective Projective
Model M at t=1
c (Image center, ox,oy)
F=focal length
image
Oc=(0,0,0)
(Camera center)
Yc-axis
Zc-axis
Xc-axis
v-axis
u-axis
(X,Y,Z)
(u,v)
Camera
Coordinates.
World Coordinates
Yw
Zw
Xw
Rc,
Tc
Principal axis
OW=(0,0,0)
(World center)
Notes: There are many useful parameters that you need to know.
The most important parameters are:
Focal length
Camera center
Other useful parameters are:
Principal axis
Image center

## Slide 6: Inspection exercise
Explain what are these variables.
  F =(focal length)
  C=(ox,oy)
  Zc = principal axis
  Ow =Camera center
  (u,v) image 2-D axes
  (Xc,Yc,Zc) 3-D axes
Focal length is the length between the lens and the image (screen)
Camera center is the origin of the camera coordinate system
Principal axis is the vector perpendicular to the image and intersects with the camera center
Image Center is the center the 2D image , or the point that the principal axis intersects with the image

## Slide 7: The most important concept for a camera is the image formation process
3D Object points (Xw,Yw,Zw): world coordinates
Step2:
Projection of camera (F)
Result  image (x,y)
Step1:
Motion of camera (Rcam=Rc-1,Tcam)
Camera Coordinates
result  Xc,Yc,Zc

## Slide 8: Step1
Motion of camera (Rcam,Tcam) Camera Coordinates
result  Xc,Yc,Zc
Yc
Zc
Xc
Xw
Zw
Yw
Rcam=(Rc)-1, and Tcam=Tc
Right-hand coordinates
(world coordinates)
Positive rotation angle about an axis: The thumb is pointing to the axis direction, a positive rotation angle is the same direction as the other fingers.
Thumb pointing Axis direction
y
x
Camera coordinates
z
Notes: We have two coordinate systems,
(i) Camera coordinate system and (ii) world coordinate system.
The realtion between these two systems is Rc and Tc as shown

## Slide 9: Rotation notations: Roll pitch yaw in aviation systems They are the same system– (you will see it if you turn the plane up side down). It is called the Right hand system.
Xw
Right-hand coordinates
Yw (Yaw angle)
Zw (Roll angle)
Xw (Pitch angle)
http://www.grc.nasa.gov/WWW/k-12/airplane/rotations.html
Zw
Yw
y
x
z

## Slide 10: A revision of basic matrix operations in case you forgot them
%matlab
A=[1 3 8
6 2 -9
10 7 5]
B=[2 1 0
7 -2 -1
3 4 6]
A’
A*B
A+B
Answer:>>
A’=
1 6 10
3 2 7
8 -9 5
A*B=
47 27 45
-1 -34 -56
84 16 23
A+B=
3 4 8
13 0 -10
13 11 11

## Slide 11: Relate world 3D to camera 3D coordinates
Pw=World 3D coordinates=[Xw,Yw,Zw]T
Pc= Camera 3D coordinates =[Xc,Yc,Zc] T
Rcam=rotate of the camera in world coord.
Tcam=Tc=translation of the camera in world coord.
We will show later why Rc is more convenient to be used

## Slide 12: Step1:Motion of camera from world to camera coordinates
Camera motion (rotation=Rcam=Rc-1, translation=Tc) will cause change of pixel position (x,y), See p156[1]
Cameras v.3d
Yc
Zc
Xc
Rcam,Tc
World center
Camera center
Xw
Zw
Yw
y
x
z

## Slide 13: To learn more about : Rotation and Translation

## Slide 14: Step2
Projection of camera (F)
Result  image (x,y)

## Slide 15: Step2: Camera coordinates to image plane (Perspective projection of camera in meters)
x=F*Xc /Zc---(1)
y=F*Yc /Zc---(2)
F=focal length in meters
A Point in 3D space (camera reference space) is [Xc,Yc,Zc]T in meters
The 2D image point is [x,y]T in meters
Notes: Step2 is about projection.

## Slide 16: Worksheet 2.1
F=5mm
Z=1 meter
A tree is 2 meters high,0.5 meters wide. What is the size of the tree appears in the image?
Sketch the diagram.
Answer:___________

## Slide 17: Picture element (Pixel) based image
[x,y]T is in meters, []T is transposition in matrix
[u,v]T in pixels which is easy to be measured by the camera
Each pixel is Sx wide and Sy high
Typically Sx = Sy =5.46um (1um=1x10^-6m=1 micron)
Sy=5.46um
Sx =5.46um
Image=
1024x768
pixles
1 pixel
CCD Charge-coupled device
Sensor: http://en.wikipedia.org/wiki/Charge-coupled_device
Notes: Of course we can measure everything in meters, but it would be easier if we measure them in picture elements (pixels), because pictures are turns into pixels in picture files.
I.e. a jpg file is 1024x768 , meaning 1024 pixels horizontally and 768 pixels vertically.
Each pixel is a point on the image CCD sensor, it responses to the light received at that picture element pixel position.

## Slide 18: Worksheet 2.2
For an image of 1280x1024 Sx = Sy =5.2um.
What is the size of the image (CMOS or CCD sensor)?
Find the pixel size of your favorite camera.
Answer:________________
Image
(CMOS
sensor)
www.ovt.com
OVT CameraChip OV9620/9120 webcam camera chip
Hint:
Notes: You can check with www.ovt.com
To see the specifications of various cameras.

## Slide 19: Image center
In picture files, usually no negative pixel is used because the origin is at one of the corners (e.g. the right bottom (1,1))
Center of CCD is placed at C= (Ox,Oy)
CCD
u (pixels)
v (pixels)
(Ox,Oy)=
(512,384) in pixels
x
1,1
1024
768
Notes: The image center is at the mid-point of the CCD, so if the CCD is 1024x768, image center is (1024/2,768/2)=(512,384)
But it is not always true because, placing the center of the CCD at the center of the projected image precisely is difficult if the cameras are mass produced. We will deal with this problem later in this chapter.

## Slide 20: CCD Pixel (u,v) based Perspective Projection
(ox,oy) in pixels is the image center
Equ. (1), (2) is divided by sx ,sy, resp.
Recall x=F*Xc /Zc---(1)
y=F*Yc /Zc---(2)
u=(F/sx)*(Xc/Zc) + ox -------(3),F is in meter, F/Sx is in pixels
v=(F/sy)*(Yc/Zc) + oy -------(4), F/Sx is in pixels
u=x/sx + ox , v=y/ sx+ oy (in pixels)
A Point in 3D space is [Xc,Yc,Zc]T in meters (or pixels , still ok, because Xc/Zc and Yc/Zc are ratios.
The 2D image point is [u,v]T in pixels

## Slide 21: Examples, center of CCD is at image center (right hand coordinate system with ideal CCD)
CCD
u (pixels)
v (pixels)
(Ox,Oy)=
(512,384) in pixels
y
x
Z
1,1
1024
768

## Slide 22: A summary
The focal length can be expressed in pixels, f=F/Sx (assume Sx=Sy)
A 3D feature point is at P=(Xc,Yc,Zc)
The center of the CCD sensor is placed at Ox,Oy in pixels of the image.
The projected image point of P=(Xc,Yc,Zc) is at (u,v)
We can use Intrinsic parameters to represent all these.

## Slide 23: Camera parameters
Intrinsic parameters
  Focal length (F) in meters,
  pixel width, height are sx sy in meters, resp.
  image (or principal) center (ox,oy) in pixels
  lens-distortion (K) (assign no distortion , ignored here).
Extrinsic parameters
  Position of the camera such as
  (Rc -- rotation, Tc -- translation)

## Slide 24: Intrinsic parameters from camera coordinates to image coordinates
Mint ( a 3x3 matrix)
(Current discussion assumes
center of camera=center of world)
Notes: We now summarize all parameters that concerns the static part of the camera and call them intrinsic parameters.
They are called intrinsic parameters because they describe the internal parts of the camera after it is produced, they are fixed if the camera is a fixed focal length camera.
But for a zoomed camera (not fixed focal length camera) the focal length may change dynamically by the user during operations.

## Slide 25: Typical webcam Intrinsic parameters
Fixed: by manufacturer
  E.g. sx =sy  5.46um (1um=1x10^-6 m=1 micron)
  For a CCD of 1024x768 , the image center or principal center is at (ox,oy)=(512x384)
  lens-distortion (K) for fixed lens. (ignore to make life easier)
Variable :
  focal length (e.g. f  5mm) , may be varied (zoom lens),
  lens-distortion (K) may follow f.
Notes: lens-distortion is not considered for this course, assume your camera is close to a pin hole camera and lens are of very good quality.

## Slide 26: Intrinsic parameters Mint (an upper-triangular matrix)
3D=Xc,Yc,Zc in meters
Image=u,v in pixels
s= arbitrary rating factor
Exercise:
Show equations (3) (4) are the same as this matrix form eq(5).
Recall:
u=(F/sx)*(Xc/Zc) + ox --(3)
v=(F/sy)*(Yc/Zc) + oy --(4)
Answer: from (5) use matrix multiplication
s*u=(F/sx)*(Xc) + ox *Zc--(i)
s*v=(F/sy)*(Yc) + oy *Zc--(ii)
s= Zc-------------------------(iii)
(i)/(iii), hence u=(F/sx)*(Xc/Zc) + ox , same as (3)
(ii)/(iii), hence v=(F/sy)*(Yc/Zc) + oy , same as (4) (proved!)
Notes: Equation 3 and 4 have been shown before, we can convert them into a matrix form in equation 5, you may try to show the conversion as an exercise.
Equation 5 has an advantage over formula 3 and 4, equation 5 is a linear system, in computer science we love linear systems because you can find a lot of math tools to solve linear problems.
Equation 3,4 are non-linear, because they involve division terms (1/Z) and make them difficult to solve.
But there is a hitch, (u,v) are what we want to find but the left hand side of the equation is a 3x1 vector [s*u,s*v,s]’ =[su,sv,s]’ , when you want to get u,v you need to do
u=su/s=first element of [su,sv,s]’ / last element of [su,sv,s]’
v=sv/s=second element of [su,sv,s]’ / last element of [su,sv,s]’
In fact we just delay the non-linear operation (the division operation) at the end. But we can use linear system math-tools to handle the more difficult stages and find u,v at the final step.
We call (u,v) as homogenous coordinates, remember that the actual pixel coordinates is (u,v) not su and sv.

## Slide 27: Simplified Intrinsic parameters Mint in pixels Sx=Sy and F/sx= f in pixels
3D=Xc,Yc,Zc in meters
Image=u,v in pixels
s= arbitrary rating factor

## Slide 28: Examples, center of CCD is at image center (right hand coordinate system with ideal CCD)
CCD
u (pixels)
v (pixels)
(Ox,Oy)=
(512,384) in pixels
y
x
Z
1,1
1024
768

## Slide 29: Worksheet 2.3
The camera CCD has 1024 x 768 pixels and the size of the CCD is 5mm x 3.75mm
What are Sx,Sy (pixel size)?
Ans:____________

## Slide 30: Exercise 2.4, 3D projection on image (Ch1_e1.m )
sx=sy=5.4um
(ox,oy)=(512,384) in pixels
f=4.3mm/5.4um=800 pixels
[Xc,Yc,Zc]T =[0.02,0.05,1.2]Tmeters
[u v]’=??
Answer: ___________
Write a pseudo code (or matlab) program to calculate the projected point [u v] T from [Xc,Yc,Zc]T based on the above camera intrinsic parameters.

## Slide 31: CCD is glued to the back of a camera
Ideally the CCD center is at ([512, 384]= image center) of a 1024x768 resolution camera.
Because of manufacturing fault the CCD center may not be at the image center.
Examples: 2 cameras of the same model (e.g. G11).
CCD
sensor
CCD
sensor
Camera 2: The sensor slight shifted to leftward and upward
Camera 1
W2 begins
Notes: We mentioned this problem before, now here is the solution.

## Slide 32: Worksheet 2.5 Because of manufacturing fault the CCD center may not be at image center, see(Ch1_e2.m )
Sx=sy=5.4um
(Ox,oy)=(600,400) in pixels
f=4.3mm/5.4um=800 pixels
[Xc,Yc,Zc]T=[0.02,0.05,1.2]T meters
[u v]T=??
Answer: [u v]T =____________________
Conclusion: A 3D object point can have different image positions for different cameras (different Mint) placed at the same position.
ox,oy=600, 400
(Image center is shifted to ox,oy)
u=400
Y=384 X
Z
Y
v
X=512
(1,1)
v=600
X,Y,Z are in 3D
u,v are in 2D

## Slide 33: Worksheet 2.6: Discussion
Two canon G11 cameras are taking pictures of a static object from the same position (using the same tripod), why the pictures are not the same.
What are the differences and why?

## Slide 34: Extrinsic parameters
Mext ( a 3x4 matrix)
(Enable camera center moves away from world center)
(Week2)

## Slide 35: Extrinsic parameters Mext
External camera parameters
Move the camera to a new position

## Slide 36: The camera moves to a new position : Rotate of the camera Rcam, and translate (TC) to a new position
Yw
Xw
Zw
Zc
Xc
World coordinates
(reference)
Camera
coordinates
Yc
Rcam
Rotation
World center
Rc
Pw
Camera center
TCam= TC =camera translation
in the world coordinates
Convention used: In this chapter we rotate the camera theta_z (angle around z axis) first, then theta_y and finally theta_x.
Notes: The world coordinate system is always the reference. The camera is first placed at the world center and then translated to Tc (Tc is actual a vector in the world coordinate system).
Then it is rotated using a transformation Rc which can rotate a vector in the world coordinate system to the camera coordinate system.
What we want to know is what is a point Pw (in the world coordinate system) should be described (as Pc) in the camera coordinate system.
The answer is Pc=Rc(Pw-Tc), we are about to show it

## Slide 37: Precise definition of Rc, Tc and Rcam
  Rc: A vector Pw will appear as Pc in camera coordinates using Rc
    Pc=Rc*Pw, where a vector Pw in world coordinates is the same vector Pc in camera coordinates . Pw does not change, it is only the coordinate system changes
Rcam is the rotational matrix that rotates the principal axis (Vz) of the camera position to a new position in the world coordinates. Rcam will change Vz, but it is always in the world coord. Sys. before and after the change.
So Rcam rotates the camera but Rc is the transformation to bring a vector in the world corrd. sys to the camera corrd sys.
Rcam = (Rc) -1 (Note R-1=RT for rotation matrices)
Tcam=Tc is the translation of the camera center in the world coordinate system.
(-Tc) takes the camera center back to the world center in the world coordinate system.
Notes: We learned that a vector P in the world coordinates is described as Pc= Rc*P=Rx*Ry*Rz*P
if the coordinate system is rotated Rz in the z-axis, Ry in the y-axis and Rx-in the x-axis.

## Slide 38: Study the rotation matrix Rc Relate world 3D to camera 3D coordinates
We study pure camera rotation first
  Assume Translation (Tc) =0 (from world center to camera center)
  Pw=a stationary vector in World 3D coordinates Pw=[Xw,Yw,Zw]T
Pc=a point in camera 3D coordinates =[Xc,Yc,Zc] T
Rotation of camera is Rcam ,
  We introduce a transform Rc , such that Rc =(Rcam)-1
  Pc=Rc*Pw where a vector Pw in world coordinates is the same vector Pc in camera coordinates
  That means a vector Pw in the world coordinate system will appear as Pc=Rc*Pw in the camera coordinate system
Rotation and Translation can be treated independently
We will study Rc in the following slides
Yw
Xw
Zw
World coordinates
(reference)
Camera rotated Rcam
Rcam
=Rc-1
Pw

## Slide 39
Camera coordinates rotated z about Z-axis relative to the world coordinates
A vector Pw=[Xw,Yw,Zw]’ is in the world coordinates (blue/solid_axes) is the same vector [Xc,Yc,Zc]’ in the camera coordinates (red/dash_axes)
Z-axis is facing you
z
Xw
Yw
Yc
z
Pw
Xc=Xwcos(z)+Ywsin(z)
z
Xwcos(z)
Ywsin(z)
z
Xw
Yw
z
Pw
Xc
z
Xwsin(z)
Yc= -Xwsin(z)+Ywcos(z)
Ywcos(z)
Concentrate on Yc
Concentrate on Xc

## Slide 40: Explanation for the previous slide
Assume the camera coordinate system is rotated by z relative to the world coordinate system. A vector in the world coordinates (large blue) is (Xw,Yw) . We are not interested in Zw , because it will not be changed by rotation in the Z-axis.
Note: The large blue vector Pw is not changed, the only change here is the camera coordinate system (rotated z against the z-axis). And the same (large blue) Pw vector as observed in the camera coordinate system is (Xc,Yc)
The left-hand diagram shows that the relation between Xc and (Xw,Yw, and z), which is Xc=Xwcos(z)+Ywsin(z)
The right-hand diagram shows that Yc= -Xwsin(z)+Ywcos(z)
And Zw = Zc , because there is no change of value in the z-axis.
So it generates the matrix formula at the top
Copied here for your reference:
That means a vector Pw in the world coordinate system will appear as Pc=Rc*Pw in the camera coordinate system.
Or it means [Xc,Yc,Zc]’=Rz*[Xw,Yw,Zw]’ in the camera coordinate system refers to the same vector as [Xw,Yw,Zw]’ in the world coordinate system.
Remember that Pc=[Xc,Yc,Zc]’ is a vector in the camera coordinate system and Pw=[Xw,Yw,Zw]’ is a vector in the world coordinate system.

## Slide 41: Given rotation angles of a camera find Rc=RxRyRz A point in World Pw=[Xw,Yw,Zw]’ is the same as Pc=[Xc,Yc,Zc]’ in the camera coordinates by these transformations
Proved in the previous slide
You may prove the other 2 cases as an exercise
http://ccar.colorado.edu/ASEN5070/handouts/coordsys.htm
http://www.google.com.hk/url?sa=t&rct=j&q=&esrc=s&source=web&cd=1&ved=0CCwQFjAA&url=http%3A%2F%2Fwww.colorado.edu%2FASEN%2Fasen3200%2Fhandouts%2FCoordinateTransformations.doc&ei=nAfdUfTzBqWSiQeo-oCYDw&usg=AFQjCNGp5O37pYqGghl5Fft1skUmSXJ2-A&sig2=6q91UADC3ZZreVm_frd7rg&bvm=bv.48705608,d.aGc&cad=rja

## Slide 42: Combine rotations in 3 axes: The camera has rotated (x, y, z), Rc brings a vector in world coordinates to the camera coordinates
Convention used: In this chapter we rotate the camera an_z (angle around z axis) first, then an_y and finally an_x.
We use Rc=Rc(xyz) for this chapter and demo programs
Notes: According the formula Rc=Rx*Ry*Rz, the camera rotations must be in this order: first rotate in z-axis , then y-axis , finally x-axis. See that Rz is closest to [Xw,Yw,Zw]’ , hence it is rotated first.
Make sure your camera is rotated in this way, then you can use the above formula.
You may use another camera rotation sequence but you must change the formula .
E.g. If first rotate in x-axis , then y-axis , finally z-axis you should use the formula Rc=Rz*Ry*Rx

## Slide 43: Another rotation possibility: How about Rc=Rc_zyx? Here we use Rc_zyx (rotate x –axis first, then y the z) Here we show formulas of Rc_zyx, and Inverse(Rc_zyx)
If we need Rc_zyx (rotate against x-axis first…),the coord. change rotation matrix
and (Rc_zyx)-1 the camera motion rotation matrix (proved in previous slides, around p39). (Note R-1=RT for rotation matrices R.)
This (Rc_zyx)-1 is the rotation matrix used in P333 of Intro. Techno. For 3-D comp. vision by Trucco and verri.
Show Rc(zyx) this for your curiosity!
Notes: According the formula Rc=Rx*Ry*Rz, the camera rotations must be in this order: first rotate in z-axis , then y-axis , finally x-axis. See that Rz is closest to [Xw,Yw,Zw]’ , hence it is rotated first.
Make sure your camera is rotated in this way, then you can use the above formula.
You may use another camera rotation sequence but you must change the formula .
E.g. If first rotate in x-axis , then y-axis , finally z-axis you should use the formula Rc=Rz*Ry*Rx

## Slide 44: Matlab program for Rc Used the Matlab/symbolic processor to create the transformation matrix
% ---- matlab demo: camera position change ----------------------
%Init position of the camera
%A camera is normally at eye(3)(Identity matrix of 3x3), no rotate in world coord.sys,
%rotated vs 3 axes: an_x,an_y,an_z (an_z first, an_y second, an_x third here),to a new (camera) coord sys.
%Rc will bring a vector in world coord. to camera coord. Such that
%so Pc=Rc*Pw, Pw is a vector in world, Pc is the same vector in cam. sys.
syms an_x an_y an_z
Rz=[cos(an_z) sin(an_z) 0
-sin(an_z) cos(an_z) 0
0 0 1]
Ry=[cos(an_y) 0 -sin(an_y)
0 1 0
sin(an_y) 0 cos(an_y)]
Rx=[1 0 0
0 cos(an_x) sin(an_x)
0 -sin(an_x) cos(an_x)]
Rc = Rx*Ry*Rz
%Properties transpose(R)*R=I, inverse(R)*R=I, inverse(R)=transpose(R), det(R)=I .
% Rc =
% [ cos(an_y)*cos(an_z), cos(an_y)*sin(an_z), -sin(an_y)]
% [ cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_y)*sin(an_x)]
% [ sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x), cos(an_x)*cos(an_y)]

## Slide 45: Study the rotation matrix Rc and Translation vector Tc Mext (3x4)Matrix form When Tc is not Zero
Yw
Xw
Zw
Zc
Xc
World coordinates
(reference)
Camera
coordinates
Yc
World center
Pw
Camera center
TC= camera translation
Rcam=(Rc)-1
Notes: After studying the effect of pure camera rotation where Tc=0, we now study the problem when the camera has translation Tc.
From the diagram you should observe that , the vector from the camera (camera center) to the top of the Christmas tree is equal to Pw-Tc.
So now we have a vector (Pw-Tc, from the camera center to the Christmas tree top) in the world coordinates,
we want to know how the vector is described in the camera coordinate system, so Rc is no used.
We learned that a vector P in the world coordinates is described as Pc= Rc*P=Rx*Ry*Rz*P
if the coordinate system is rotated Rz in the z-axis, Ry in the y-axis and Rx-in the x-axis.
Hence the total transformation (combining translation and rotation) becomes Pc=Rc(Pw-Tc)
That means a point Pw in the world coordinates is the same point Pc in the camera coordinates if the camera is translated and rotated.

## Slide 46: Combine Mint and Mext
Projection
Mint=
Camera
motion
R,T
Mext=
Rc[I3| -Tc]
Image
u,v
World
Coord.
Xw
Yw
Zw
Camera
Coord.
Xc
Yc
Zc

## Slide 47: Take home exercise
Given the camera rotation angles are:
  an_z is the rotation about the Z-axis.
  an_y is the rotation about the Y-axis.
  an_x is the rotation about the X-axis.
and the camera translation Tc=[tcx,tcy,tcz]’
Test using matlab to verify the Properties
  RT*R=I,R-1*R=I, R-1=RT, det(R)=I are true
Write a matlab (or pseudo code) program to find [Xc,Yc,Zc]T from [Xw,Yw,Zw]T

## Slide 48: Projection Combine Mint and Mext to become P

## Slide 49: Conclusion
Studied camera model intrinsic parameters
Studied camera rotation matrix R
Studied camera translation matrix T
Studied camera projection matrix P
49

## Slide 50: References
[1A] Hartley and Zisserman, Multiple geometry in computer vision, Cambridge, University Press. 2004 (2nd edition, paperback).
[1B] Hartley and Zisserman, Multiple geometry in computer vision, Cambridge, University Press. 1999 (1st edition, hardback).
[2] CVonline: http://homepages.inf.ed.ac.uk/rbf/CVonline
[3] On Skew Symmetric matrix http://mathworld.wolfram.com/SkewSymmetricMatrix.html
[4] On Skew Symmetric matrix http://www.ee.ic.ac.uk/hp/staff/dmb/matrix/special.html#Skew_Symmetric
[5]On RQ decomposition http://wwwcsif.cs.ucdavis.edu/~wangjj/gsvd/codes/rq5.m
[6] Camera calibration matlab toolbox http://www.vision.caltech.edu/bouguetj/calib_doc/index.html#examples
[7] OpenGL Angles to Axes: http://www.songho.ca/opengl/gl_anglestoaxes.html
[8] http://www.ewerksinc.com/refdocs/coordinate%20and%20unit%20vector.pdf
[9] coordinate systems http://www.colorado.edu/ASEN/asen3200/handouts/
[10]http://www.google.com.hk/url?sa=t&rct=j&q=&esrc=s&source=web&cd=1&ved=0CCwQFjAA&url=http%3A%2F%2Fwww.colorado.edu%2FASEN%2Fasen3200%2Fhandouts%2FCoordinateTransformations.doc&ei=nAfdUfTzBqWSiQeo-oCYDw&usg=AFQjCNGp5O37pYqGghl5Fft1skUmSXJ2-A&sig2=6q91UADC3ZZreVm_frd7rg&bvm=bv.48705608,d.aGc&cad=rja
50

## Slide 51: End

## Slide 52: Appendix 1
Some text like to use Rcam rather than Rc, we will see the difference.
Cameras v.3a
52

## Slide 53: Precise definition of Rc, Tc and Rcam
  Rc: A vector (V) Pw will appear as Pc in camera coordinates using Rc
    Pc=Rc*Pw , where a vector Pw in world coordinates is the same vector Pc in camera coordinates . V does not change, it is only the coordinate system changes
Rcam is the rotational matrix that rotates the principal axis (Vz) of the camera position to a new position in the world coordinates. Rcam will change Vz, but it is always in the world coord. Sys. before and after the change.
So Rcam rotates the camera but Rc is the transform to bring a vector in the world corrd. sys to the camera corrd sys.
Rcam = (Rc) -1 (Note R-1=RT for rotation matrices)
Tcam=Tc is the translation of the camera center in the world coordinate system.
(-Tc) takes the camera center back to the world center in the world coordinate system.
Notes: We learned that a vector P in the world coordinates is described as Pc= Rc*P=Rx*Ry*Rz*P
if the coordinate system is rotated Rz in the z-axis, Ry in the y-axis and Rx-in the x-axis.

## Slide 54: To rotate a vector in 2D
The vector ux [1,0]’ is rotated by the matrix R() to become
  x’=cos(), y’=sin()
The vector uy [0,1]’ is rotated by the matrix R() to become
  x’’= -sin(), y’’= cos()
A general vector v is a combination of
  x component (vx) * ux and
  y component (vy) * uy
So, v is rotated to v’ by R() to produce x’+x’’ in x and y’+ y’’ in y
http://reedbeta.wordpress.com/2011/09/18/rotations-and-infinitesimal-generators/

-
cos()
sin()
Radius=1
-sin()
cos()
uy
ux

## Slide 55
To show Rcam = Rc-1
a=0.3 %matlab demo:
Rc_pos_a=[cos(a) sin(a) 0
-sin(a) cos(a) 0
0 0 1]
Rcam=[cos(a) -sin(a) 0
sin(a) cos(a) 0
0 0 1]
Rc_pos_a*Rcam %it is I3
z
Xw
Yw
Yc
z
Xc
We can think of Rcam(Z)rotates the camera pointing to Yw in the world coordinate system to a new direction of Yc. Using the result of vector rotation described in the last slide we can show that Rcam(Z)=Rc(Z)-1
(Note R-1=RT for rotation matrices R.)

## Slide 56: This slide is shown earlier combine rotations in 3 axes: The camera has rotated (x, y, z), Rc brings a vector in world coordinates to the camera coordinates
Notes: According the formula Rc=Rx*Ry*Rz, the camera rotations must be in this order: first rotate in z-axis , then y-axis , finally x-axis. See that Rz is closest to [Xw,Yw,Zw]’ , hence it is rotated first.
Make sure your camera is rotated in this way, then you can use the above formula.
You may use another camera rotation sequence but you must change the formula .
E.g. If first rotate in x-axis , then y-axis , finally z-axis you should use the formula Rc=Rz*Ry*Rx

## Slide 57: Rc=Rc_xyz, Here we use Rc_zyx (rotate x –axis first, then y the z) Here we show Rc_zyx, and Inverse(Rc_zyx)
If we need Rc_zyx (rotate against x-axis first) which is the coordinate change rotation matrix
and (Rc_zyx)-1 is the camera motion rotation matrix (proved in previous slides, around p39) (Note R-1=RT for rotation matrices R.)
This (Rc_zyx)-1 is the rotation matrix used in P333 of Intro. Techno. For 3-D comp. vision by Trucco and verri.
(Note R-1=RT for rotation matrices R.)
Notes: According the formula Rc=Rx*Ry*Rz, the camera rotations must be in this order: first rotate in z-axis , then y-axis , finally x-axis. See that Rz is closest to [Xw,Yw,Zw]’ , hence it is rotated first.
Make sure your camera is rotated in this way, then you can use the above formula.
You may use another camera rotation sequence but you must change the formula .
E.g. If first rotate in x-axis , then y-axis , finally z-axis you should use the formula Rc=Rz*Ry*Rx

## Slide 58
syms an_x an_y an_z
%----------------------------------
Rz=[cos(an_z) sin(an_z) 0
-sin(an_z) cos(an_z) 0
0 0 1]
%---------------------------------------
Ry=[cos(an_y) 0 -sin(an_y)
0 1 0
sin(an_y) 0 cos(an_y)]
%-------------------------------------
Rx=[1 0 0
0 cos(an_x) sin(an_x)
0 -sin(an_x) cos(an_x)]
%-----------------------------------------
'This is to show the following 3 important results'
Rxyz=Rx*Ry*Rz
Rzyx=Rz*Ry*Rx
inv_Rzyx=inv(Rzyx)
%inv_Rzyx is used in P333 of Trucco
Result: -------------
Rxyz =
[ cos(an_y)*cos(an_z), cos(an_y)*sin(an_z), -sin(an_y)]
[ cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x), cos(an_x)*cos(an_y)]
Rzyx =
[ cos(an_y)*cos(an_z), cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y)]
[ -cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z)]
[ sin(an_y), -cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]
inv_Rzyx =
[ cos(an_y)*cos(an_z), -cos(an_y)*sin(an_z), sin(an_y)]
[ cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), -cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z), cos(an_x)*cos(an_y)]

## Slide 59: %show transpose(Rc_pos_a)=Rc_neg_a and Rc_pos_a *transpose(Rc_pos_a) =I
a=0.3 %any angle a is ok
'Rc_pos_a is '
Rc_pos_a=[cos(a) sin(a) 0
-sin(a) cos(a) 0
0 0 1]
'transpose (Rc_pos_a is) '
Rc_pos_a'
'Rc_neg_a is '
Rc_neg_a=[cos(-a) sin(-a) 0
-sin(-a) cos(-a) 0
0 0 1]
‘shown: transpose(Rc_pos_a)=Rc_neg_a '
'------------------------------------------------'
'show that Rc_pos_a*transpose(Rc_pos_a)=I '
Rc_pos_a*Rc_pos_a'
% '----------results--------'
% a = 0.3000
%Rc_pos_a =
% 0.9553 0.2955 0
% -0.2955 0.9553 0
% 0 0 1.0000
% transpose (Rc_pos_a is)
% 0.9553 -0.2955 0
% 0.2955 0.9553 0
% 0 0 1.0000
% Rc_neg_a =
% 0.9553 -0.2955 0
% 0.2955 0.9553 0
% 0 0 1.0000
% shown: transpose(Rc_pos_a)=Rc_neg_a
% show that Rc_pos_a*transpose(Rc_pos_a)=I
% 1 0 0
% 0 1 0
% 0 0 1

## Slide 60: Practical issue: center of CCD is at image center (right hand coordinate system with realistic CCD) **Image origin at left-top corner for .bmp .jpg etc. ‘-f’ instead of ‘f’
CCD
u (pixels)
v (pixels)
(Ox,Oy)=
(512,384) in pixels
y
x
Z
1,1
1024
768

## Slide 61: Summary and meanings of notations used in this chapter
  Pw=a vector in the world coordinate system.
  Pc= the same vector (as Pw) but in the camera coordinate system.
  Rcam, Tc : rotation, translation, resp., in the world coord. sys.
  Rc : After the camera is rotated Rcam and translated Tc in the world coordinate system, Pc=Rc*(Pw-Tc)-----(i)
  We proved that Rcam=Rc-1, so equation (i) becomes
  Pc=(Rcam)-1*(Pw-Tc)----(ii), or
  Pc=(Rcam)-1*(Pw)+ (-(Rcam)-1*Tc)----(ii), so we can make
  Pc=R*Pw+T---(iii), if
    R=(Rcam)-1=Rc and
    T=(-(Rcam)-1*Tc) = -Rc*Tc
Equation (iii) is an expression used in many articles.

## Slide 62: rot_syms.m : use the matlab symbolic processor to show varies possible arrangements of the Rotational matrix
% rot_syms.m
%show varies arrangement of the
%R rotation matrix, khw 140319
syms an_x an_y an_z real
Rz=[cos(an_z) sin(an_z) 0
-sin(an_z) cos(an_z) 0
0 0 1];
Ry=[cos(an_y) 0 -sin(an_y)
0 1 0
sin(an_y) 0 cos(an_y)];
Rx=[1 0 0
0 cos(an_x) sin(an_x)
0 -sin(an_x) cos(an_x)];
Rxyz= Rz*Ry*Rx %do x first then y, z
transpose_Rxyz= (Rz*Ry*Rx)'
inverse_Rxyz= inv(Rz*Ry*Rx)
Rzyx= Rx*Ry*Rz %do z first then y, x
transpose_Rzyx= (Rx*Ry*Rz)' %do z first, then z, and y
inverse_Rzyx= inv(Rx*Ry*Rz)%do z first, then z, and y
%ANOTHER SET , IN THIS SET r_x=Rx', r_y=Ry', r_z=Rz'
rz=Rz';
ry=Ry';
rx=Rx';
rxyz= rz*ry*rx %do x first then y, z
transpose_rxyz= (rz*ry*rx)'
inverse_rxyz= inv(rz*ry*rx)
rzyx= rx*ry*rz %do z first then y, x
transpose_rzyx= (rx*ry*rz)' %do z first, then z, and y
inverse_Rzyx= inv(rx*ry*rz)%do z first, then z, and y

## Slide 63: Output of rot_syms.m (page1)
>> rot_syms
Rxyz =
[ cos(an_y)*cos(an_z), cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y)]
[ -cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z)]
[ sin(an_y), -cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]
transpose_Rxyz =
[ cos(an_y)*cos(an_z), -cos(an_y)*sin(an_z), sin(an_y)]
[ cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), -cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z), cos(an_x)*cos(an_y)]
inverse_Rxyz =
[ cos(an_y)*cos(an_z), -cos(an_y)*sin(an_z), sin(an_y)]
[ cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), -cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z), cos(an_x)*cos(an_y)]
Rzyx =
[ cos(an_y)*cos(an_z), cos(an_y)*sin(an_z), -sin(an_y)]
[ cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x), cos(an_x)*cos(an_y)]
transpose_Rzyx =
[ cos(an_y)*cos(an_z), cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)]
[ cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x)]
[ -sin(an_y), cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]
inverse_Rzyx =
[ cos(an_y)*cos(an_z), cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)]
[ cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x)]
[ -sin(an_y), cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]

## Slide 64: Output of rot_syms.m (page2)
rxyz =
[ cos(an_y)*cos(an_z), cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)]
[ cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x)]
[ -sin(an_y), cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]
transpose_rxyz =
[ cos(an_y)*cos(an_z), cos(an_y)*sin(an_z), -sin(an_y)]
[ cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x), cos(an_x)*cos(an_y)]
inverse_rxyz =
[ cos(an_y)*cos(an_z), cos(an_y)*sin(an_z), -sin(an_y)]
[ cos(an_z)*sin(an_x)*sin(an_y) - cos(an_x)*sin(an_z), cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z), cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y), cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x), cos(an_x)*cos(an_y)]
rzyx =
[ cos(an_y)*cos(an_z), -cos(an_y)*sin(an_z), sin(an_y)]
[ cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), -cos(an_y)*sin(an_x)]
[ sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z), cos(an_x)*cos(an_y)]
transpose_rzyx =
[ cos(an_y)*cos(an_z), cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y)]
[ -cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z)]
[ sin(an_y), -cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]
inverse_Rzyx =
[ cos(an_y)*cos(an_z), cos(an_x)*sin(an_z) + cos(an_z)*sin(an_x)*sin(an_y), sin(an_x)*sin(an_z) - cos(an_x)*cos(an_z)*sin(an_y)]
[ -cos(an_y)*sin(an_z), cos(an_x)*cos(an_z) - sin(an_x)*sin(an_y)*sin(an_z), cos(an_z)*sin(an_x) + cos(an_x)*sin(an_y)*sin(an_z)]
[ sin(an_y), -cos(an_y)*sin(an_x), cos(an_x)*cos(an_y)]

## Slide 65: Rotation matrix

## Slide 66: Answer for Worksheet2 Image processing and computer vision
Camera models and parameters
Answers

## Slide 67: Answer: Worksheet 2.1
F=5mm
Z=1 meter
A tree is 2 meters high,0.5 meters wide. What is the size of the tree appears in the image?
Answer: using y=F*Yc /Zc
Tall=y=F*Y/Z=5x10-3x2 meters/1 meter=10mm
  or 5*2*10^-3/1 =10mm
Wide=x=F*X/Z=5x10-3x0.5 meters/1 meter=0.0025 meter=2.5mm,
  or =5*0.5*10^-3*1 =2.5mm

## Slide 68: Answer: Worksheet 2.2
For an image of 1280x1024, Sx = Sy =5.2um.
What is the size of the image (CMOS or CCD sensor)?
1280*5.2um =1280*5.2*10^-6 = 0.00666m=6.66mm
1024X5.2um =1024*5.2*10^-6 = 0.00532m=5.32mm
Image
(CMOS sensor)
www.ovt.com
OVT CameraChip OV9620/9120 webcam camera chip

## Slide 69: Answer Worksheet 2.3
The camera CCD has 1024x768 pixels and is 5mmx3.75mm
What are Sx,Sy (pixel size)?
Ans:
  Sx=5mm/1024=4.88um
  Sy=3.75mm/768=4.88um
  Why Sx=Sy? Calculate the Sx , Sy of your favorite digital camera.

## Slide 70: Answer: Worksheet 2.4, 3D projection on image (Ch1_e1.m )
sx=sy=5.4um
(ox,oy)=(512,384) in pixels
f=4.3mm/5.4um=800 pixels
[Xc,Yc,Zc]T =[0.02,0.05,1.2]Tmeters
[u v]’=??
Answer: [525.3, 717.3]T
Write a pseudo code (or matlab) program to calculate the projected point [u,v]’ from [Xc,Yc,Zc]’ based on the above camera intrinsic parameters.
%matlab
k=[800 0 512
0 8000 384
0 0 1]
x=[0.02 0.05 1.2]'
im=k*x
im(1)/im(3)
im(2)/im(3)
%answer:
im =
630.4000
860.8000
1.2000
u,v=
525.3333
717.3333

## Slide 71: Answer Worksheet 2.5 Because of manufacturing fault CCD center may not be at image center, example (Ch1_e2.m )
Sx=sy=5.4um
(Ox,oy)=(600,400) in pixels
f=4.3mm/5.4um=800 pixels
[Xc,Yc,Zc]T=[0.02,0.05,1.2]T meters
[u v]T=[613.3, 733.3]T
Conclusion: A 3D object point can have different image positions for different cameras (different Mint) placed at the same position.
ox,oy=600, 400
(Image center is shifted to ox,oy)
u=400
Y=384 X
Z
Y
v
X=512
(1,1)
v=600
X,Y,Z are in 3D
u,v are in 2D

## Slide 72: Answer: Worksheet 2.6 Discussion
Two canon G11 cameras are taking pictures of a static object from the same position (using the same tripod), why the pictures are not the same.
What are the differences and why?
  CCD are not at the same position
  Focal lengths are not the same (zooming)

## Slide 73: Tutorial exercises
Cmsc5711 : ch2 camera models

## Slide 74: CMSC5711: Tutorial 2.1 : Intrinsic parameters Mint (an upper-triangular matrix)
3D=Xc,Yc,Zc in meters
Image=u,v in pixels
s= arbitrary rating factor
Exercise:
Show equations (3) (4) are the same as this matrix form eq(5).
Recall:
u=(F/sx)*(Xc/Zc) + ox --(3)
v=(F/sy)*(Yc/Zc) + oy --(4)
Notes: Equation 3 and 4 have been shown before, we can convert them into a matrix form in equation 5, you may try to show the conversion as an exercise.
Equation 5 has an advantage over formula 3 and 4, equation 5 is a linear system, in computer science we love linear systems because you can find a lot of math tools to solve linear problems.
Equation 3,4 are non-linear, because they involve division terms (1/Z) and make them difficult to solve.
But there is a hitch, (u,v) are what we want to find but the left hand side of the equation is a 3x1 vector [s*u,s*v,s]’ =[su,sv,s]’ , when you want to get u,v you need to do
u=su/s=first element of [su,sv,s]’ / last element of [su,sv,s]’
v=sv/s=second element of [su,sv,s]’ / last element of [su,sv,s]’
In fact we just delay the non-linear operation (the division operation) at the end. But we can use linear system math-tools to handle the more difficult stages and find u,v at the final step.
We call (u,v) as homogenous coordinates, remember that the actual pixel coordinates is (u,v) not su and sv.

## Slide 75: Answer: Tutorial 2.1 Intrinsic parameters Mint (an upper-triangular matrix)
3D=Xc,Yc,Zc in meters
Image=u,v in pixels
s= arbitrary rating factor
Exercise:
Show equations (3) (4) are the same as this matrix form eq(5).
Recall:
u=(F/sx)*(Xc/Zc) + ox --(3)
v=(F/sy)*(Yc/Zc) + oy --(4)
Answer: from (5) use matrix multiplication
s*u=(F/sx)*(Xc) + ox *Zc--(i)
s*v=(F/sy)*(Yc) + oy *Zc--(ii)
s= Zc-------------------------(iii)
(i)/(iii), hence u=(F/sx)*(Xc/Zc) + ox
(i)/(iii), hence v=(F/sy)*(Yc/Zc) + oy (proved!)
Notes: Equation 3 and 4 have been shown before, we can convert them into a matrix form in equation 5, you may try to show the conversion as an exercise.
Equation 5 has an advantage over formula 3 and 4, equation 5 is a linear system, in computer science we love linear systems because you can find a lot of math tools to solve linear problems.
Equation 3,4 are non-linear, because they involve division terms (1/Z) and make them difficult to solve.
But there is a hitch, (u,v) are what we want to find but the left hand side of the equation is a 3x1 vector [s*u,s*v,s]’ =[su,sv,s]’ , when you want to get u,v you need to do
u=su/s=first element of [su,sv,s]’ / last element of [su,sv,s]’
v=sv/s=second element of [su,sv,s]’ / last element of [su,sv,s]’
In fact we just delay the non-linear operation (the division operation) at the end. But we can use linear system math-tools to handle the more difficult stages and find u,v at the final step.
We call (u,v) as homogenous coordinates, remember that the actual pixel coordinates is (u,v) not su and sv.

## Slide 76: Tutorial 2.2 Given
Focal length is 3mm, sx=sy=3um
(ox,oy)=(620,410) in pixels
A 3D point is at X=0.015 meters, Y=0.02 meters and Z=2 meters away from the camera center.
Fill in the blanks (__?)
[u v]T=??
Answer: [u v]T =____________________?
ox,oy=620, 410
(Image center is shifted to ox,oy)
u=410
Y=384 X
Z
Y
v
X=512
(1,1)
v=620
X,Y,Z are in 3D
u,v are in 2D

## Slide 77: Answer: Tutorial 2.2 Given
Focal length is 3mm, sx=sy=3um
(ox,oy)=(620,410) in pixels
A 3D point is at X=0.015 meters, Y=0.02 meters high and Z=2 meters away from the camera center.
Fill in the blanks (__?)
[u v]T=??
Answer: [u v]T =___627.5, 420_________________?
%matlab
m=[1000 0 620; 0 1000 410; 0 0 1]
p=[0.015 0.02 2]'
x=m*p
u=x(1)/x(3)
v=x(2)/x(3)
Answer :
u =627.5,v = 420
ox,oy=620, 410
(Image center is shifted to ox,oy)
u=410
Y=384 X
Z
Y
v
X=512
(1,1)
v=620
X,Y,Z are in 3D
u,v are in 2D

## Slide 78
Tutorial 2.3: Camera coordinates rotated y about Y-axis relative to the world coordinates. A vector Pw=[Xw,Yw,Zw]’ is in the world coordinates (blue/solid_axes) is the same vector [Xc,Yc,Zc]’ in the camera coordinates (red/dash_axes)
Q1: Y-axis is facing in or out of the paper?
Q2: Fill in the blanks (__?)
-y
Xw
Zw
__?
-y
Pw
Show
Xc=Xwcos(-y) +Zw_sin(-y)
-y
Xwcos(__?)
___?sin(-y)
-y
Xw
Zw
-y
Pw
Xy
-y
Xw___?(-y)
Show:Zc= -Xwsin(-y)+Zwcos(-y)
__?cos(-z)
Mark vector Pc on the paper
___?

## Slide 79
ANSWER2.3: Camera coordinates rotated y about Y-axis relative to the world coordinates. A vector Pw=[Xw,Yw,Zw]’ is in the world coordinates (blue/solid_axes) is the same vector [Xc,Yc,Zc]’ in the camera coordinates (red/dash_axes)
Q1: Y-axis is facing in or out of the paper?
Ans: in, Q2: Fill in the blanks (__?)
-y
Xw
Zw
Zc_?
-y
Pw
Show
Xc=Xwcos(-y) +Zw_sin(-y)
-y
Xwcos(-y?)
Zw_?sin(-y)
-y
Xw
Zw
-y
Pw
Xy
-y
Xwsin?(-y)
Show:Zc= -Xwsin(-y)+Zwcos(-y)
Zw?cos(-z)
Mark vector Pc on the paper
Zc_?

## Slide 80: Tutorial 2.4: Study the rotation matrix Rc and Translation vector Tc Mext (3x4)Matrix form When Tc is not Zero
Yw
Xw
Zw
Zc
Xc
World coordinates
(reference)
Camera
coordinates
Yc
World center
Pw
Camera center
TC= camera translation
Rcam=(Rc)-1
Tutorial 2.5:
Show the dimensions of the variables.
Notes: After studying the effect of pure camera rotation where Tc=0, we now study the problem when the camera has translation Tc.
From the diagram you should observe that , the vector from the camera (camera center) to the top of the Christmas tree is equal to Pw-Tc.
So now we have a vector (Pw-Tc, from the camera center to the Christmas tree top) in the world coordinates,
we want to know how the vector is described in the camera coordinate system, so Rc is no used.
We learned that a vector P in the world coordinates is described as Pc= Rc*P=Rx*Ry*Rz*P
if the coordinate system is rotated Rz in the z-axis, Ry in the y-axis and Rx-in the x-axis.
Hence the total transformation (combining translation and rotation) becomes Pc=Rc(Pw-Tc)
That means a point Pw in the world coordinates is the same point Pc in the camera coordinates if the camera is translated and rotated.

## Slide 81: ANSWER2.4: Study the rotation matrix Rc and Translation vector Tc Mext (3x4)Matrix form When Tc is not Zero
Yw
Xw
Zw
Zc
Xc
World coordinates
(reference)
Camera
coordinates
Yc
World center
Pw
Camera center
TC= camera translation
Rcam=(Rc)-1
Exercise 2.2:
Show the dimensions
of the variables.
Answer
Notes: After studying the effect of pure camera rotation where Tc=0, we now study the problem when the camera has translation Tc.
From the diagram you should observe that , the vector from the camera (camera center) to the top of the Christmas tree is equal to Pw-Tc.
So now we have a vector (Pw-Tc, from the camera center to the Christmas tree top) in the world coordinates,
we want to know how the vector is described in the camera coordinate system, so Rc is no used.
We learned that a vector P in the world coordinates is described as Pc= Rc*P=Rx*Ry*Rz*P
if the coordinate system is rotated Rz in the z-axis, Ry in the y-axis and Rx-in the x-axis.
Hence the total transformation (combining translation and rotation) becomes Pc=Rc(Pw-Tc)
That means a point Pw in the world coordinates is the same point Pc in the camera coordinates if the camera is translated and rotated.

## Slide 82: Tutorial 2.5
Write Mexti=1,2,3; j=1,2,3,4 in terms of Ri=1,2,3;j=1,2,3 and Tc=[tcx ,tcy ,tcz]T

## Slide 83: Answer for Tutorial 2.5 (i)
%Matlab code
%Worksheet 2.7(i) Write Mi=1,2,3; %j=1,2,3,4 in terms of
%Ri=1,2,3;j=1,2,3 and %tc=[tcx;tcy;tcz]
clear
syms Mext Rc tcx tcy tcz r11 r12 r13 r21 r22 r23 r31 r32 r33
Rc=[ r11 r12 r13; r21 r22 r23; r31 r32 r33]
Tc=[tcx ;tcy ;tcz]
'%%% answer ws 2.7 (i) %%%%%%%%%%'
'now look at the answers for ws 2.7(i)'
Mext=Rc*[eye(3) -1*Tc]
'size of Mext is '
size(Mext)
'kit any key to continue'
pause
Answer:
Mext =
[ r11, r12, r13, - r11*tcx - r12*tcy - r13*tcz]
[ r21, r22, r23, - r21*tcx - r22*tcy - r23*tcz]
[ r31, r32, r33, - r31*tcx - r32*tcy - r33*tcz]

## Slide 84: Tutorial 2.6
If the camera has moved Tc=[tcx ,tcy ,tcz]T
and rotates z first , y second and then x in the world camera, discuss the procedures to find Mexti=1,2,3; j=1,2,3,4

## Slide 85: Answer: Tutorial 2.6
If the camera has moved Tc=[tcx,tcy,tcz]T
and rotates z first , y second and then z in the world camera, discuss how do you find Mexti=1,2,3; j=1,2,3,4
Answer:
Find Rc first (see below), then find Mext as in the previous exercise.

## Slide 86: Answer for 2.6 (i)
%Matlab code
%Worksheet 2.7(i) Write Mi=1,2,3; %j=1,2,3,4 in terms of
%Ri=1,2,3;j=1,2,3 and %tc=[tcx;tcy;tcz]
clear
syms Mext Rc tcx tcy tcz r11 r12 r13 r21 r22 r23 r31 r32 r33
Rc=[ r11 r12 r13; r21 r22 r23; r31 r32 r33]
Tc=[tcx ;tcy ;tcz]
'%%% answer ws 2.7 (i) %%%%%%%%%%'
'now look at the answers for ws 2.7(i)'
Mext=Rc*[eye(3) -1*Tc]
'size of Mext is '
size(Mext)
'kit any key to continue'
pause
Answer:
Mext =
[ r11, r12, r13, - r11*tcx - r12*tcy - r13*tcz]
[ r21, r22, r23, - r21*tcx - r22*tcy - r23*tcz]
[ r31, r32, r33, - r31*tcx - r32*tcy - r33*tcz]

## Slide 87: Answer for 2.6 (ii)
clear
%'Worksheet 2.7(ii) If the camera has moved
disp('Tt=1,2,3 and rotates an_x, an_y, anz in the world camera, ')
disp('find Mi=1,2,3; j=1,2,3,4')
syms P Mint Mext f ox oy tcx tcy tcz r11 r12 r13 r21 r22 r23 r31 r32 r33 an_x an_y an_z
Rz=[cos(an_z) sin(an_z) 0
-sin(an_z) cos(an_z) 0
0 0 1];
Ry=[cos(an_y) 0 -sin(an_y)
0 1 0
sin(an_y) 0 cos(an_y)];
Rx=[1 0 0
0 cos(an_x) sin(an_x)
0 -sin(an_x) cos(an_x)]
Tc=[tcx ;tcy ;tcz]
Rc=Rx*Ry*Rz
Mext=Rc*[eye(3) -1*Tc]
Mint=[-f 0 ox; 0 f oy; 0 0 1]
'%%%%% answer ws 2.7 (ii) %%%%%%%%%%%%%'
'now look at the answers for 2.7 (ii)'
P=Mint*Mext
'P(:,1)------- first column'
P(:,1)
'P(:,2)------- second column'
P(:,2)
'P(:,3)------- third column'
P(:,3)
'size of P is '
size(P)

## Slide 88: Answer for 2.6 (ii)
%Answer:
P(:,1)------------first column----------------------------------
ans =
ox*(sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)) - f*cos(an_y)*cos(an_z)
oy*(sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)) - f*(cos(an_x)*sin(an_z) - cos(an_z)*sin(an_x)*sin(an_y))
sin(an_x)*sin(an_z) + cos(an_x)*cos(an_z)*sin(an_y)
P(:,2) -----------second column--------------------------------
ans =
- ox*(cos(an_z)*sin(an_x) - cos(an_x)*sin(an_y)*sin(an_z)) - f*cos(an_y)*sin(an_z)
f*(cos(an_x)*cos(an_z) + sin(an_x)*sin(an_y)*sin(an_z)) - oy*(cos(an_z)*sin(an_x) - cos(an_x)*sin(an_y)*sin(an_z))
cos(an_x)*sin(an_y)*sin(an_z) - cos(an_z)*sin(an_x)
P(:,3) ------------third column-----------------------------------
ans =
f*sin(an_y) + ox*cos(an_x)*cos(an_y)
oy*cos(an_x)*cos(an_y) + f*cos(an_y)*sin(an_x)
cos(an_x)*cos(an_y)

## Slide 89: Tutorial 2.7 Write pi=1,2,3; j=1,2,3,4 in terms of Mext:i=1,2,3;j=1,2,3 and f

## Slide 90: Answer: Tutorial 2.7
%Matlab code
clear
syms Mext f M11 M12 M13 M14 M21 M22 M23 M24 M31 M32 M33 M34
Mext=[M11 M12 M13 M14 ;M21 M22 M23 M24 ;M31 M32 M33 M34]
[f 0 0 ; 0 f 0 ; 0 0 1]*Mext
% answer %%%%%%%%%%%%%%%%%%%%%%%%%%
P =
[ M11*f, M12*f, M13*f, M14*f]
[ M21*f, M22*f, M23*f, M24*f]
[ M31, M32, M33, M34]

## Slide 91: Answer for tut2.7, ref: http://www.colorado.edu/ASEN/asen3200/handouts a demo program to show the camera model (demo_cam_model6b.m)
% demo_cam_model6b.m
function demo_cam_model %
clear, xmax=1024 ,ymax=768 , xmin=1,ymin=1
anx=0,any=0,anz=0
command=0;%init
while(command ~= 'q')
command = input('Enter a command:a<, s>, w^, zv ,e(Z-axis: +ve),x(Z-axis: -ve),r(y-axis: +ve),c(y-axis: -ve),q=quit : ', 's');
switch command
case {'a'} ,any=any+5
case {'s'} ,any=any-5
case {'w'} ,anx=anx-5
case {'z'} ,anx=anx+5
case {'e'} ,anz=anz+5
case {'x'} ,anz=anz-5
case {'r'} ,any=any+5
case {'c'} ,any=any-5
otherwise ,disp('Unknown command'), end
[u,v]=rt(anx*pi/180,any*pi/180,anz*pi/180,xmax,xmin,ymax,ymin)
figure(1), clf, subplot(2,2,1),hold on
plot(xmin,ymin),plot(xmax,ymax)
plot([u],[v],'c-'),title('image point')
axis([xmin xmax ymin ymax])
set(gca,'XDir','reverse'); end
%%%%%%% rt function %%%%%
function [u,v]=rt(anx,any,anz,xmax,xmin,ymax,ymin)
%Find basic parameters----------------------------
pixel_width=5.4*10^-6 %5.4um (micron), assume square pixels
F=3*10^-3 %3mm foval length in meters
f=F/pixel_width %focal length in pixels
%assume the picture is 1024 x 768
ox=xmax/2, oy=ymax/2 %cam center is at middle
oy=ymax/2
Kint=[f 0 ox; 0 f oy; 0 0 1]
% ---- camera position change ----------------
%Init position of the camera
%A camera is normally at eye(3), no rotate io in world coord.sys,
%rotated about the 3 axes:an_x,an_y,an_z to the cam coord sys.
%Rc will bring a vector in world cood. to camera cood. Such that
%so vc=Rc*vw, vw is a vector in world, vc is same vector in cam. sys.
Rc=rot(anx,any,anz)
Tc=[0,0,0]'%camera translation

## Slide 92: Continue(answer: tut2.7)
%%%%%%%% rot fucntion %%%%%%%%%%%
%matlab : usage e.g. Rc=rot(1*pi/180, 3*pi/180, 5*pi/180) % three angles 1,3,5
function Rc=rot(an_x,an_y,an_z) %in radians
%an_x=angle rotates about the x-axis(Yaw )
%an_y=angle rotates about the y-axis (Pitch)
%an_z= angle rotates about the z-axis (Roll)
Rz=[cos(an_z) sin(an_z) 0
-sin(an_z) cos(an_z) 0
0 0 1];
Ry=[cos(an_y) 0 -sin(an_y)
0 1 0
sin(an_y) 0 cos(an_y)];
Rx=[1 0 0
0 cos(an_x) sin(an_x)
0 -sin(an_x) cos(an_x)]
Rc = Rx*Ry*Rz;
%Properties transpose(R)*R=I, inverse(R)*R=I, inverse(R)=transpose(R), det(R)=I .
% a 3D point P
xx=300 %object width
yy=300 %object height
zz=1000 %object distance from the world origin
Pw1=[0 -yy*f zz*f 1]' %P_w is at a 3D position in world coorinates
Pw2=[0 yy*f zz*f 1]' %P_w is at a 3D position in world coorinates
Pw3=[-xx*f 300*f zz*f 1]' %P_w is at a 3D point in world coord.
Pw4=[xx*f 300*f zz*f 1]' %P_w is at a 3D point in world coord.
Pw=[Pw1 Pw2 Pw3 Pw4]
%Pcam=Rcw*(Pw-Tc) %P_c is at a 3D position in cam coord.
%%---- projection----------------------
%Kext=Rc*[eye(3), -1*Tc] %eye(n) is an identity matrix of size nxn
Kext=Rc*[eye(3), -1*Tc] %eye(n) is an identity matrix of size nxn
x=Kint*Kext*[Pw]
u=x(1,:)./x(3,:), v=x(2,:)./x(3,:)
%Properties transpose(R)*R=I, inverse(R)*R=I, inverse(R)=transpose(R), det(R)=I .

## Slide 93: Tutorial 2.8
Assume that the rotation transformation Rcam =Rc-1 from the world coordinate system to camera coordinate system is
and the camera center in the world coordinates is denoted as meters.
There is a 3-D point meters in the world coordinates. Compute the 3D coordinates of this point , called Pa, at the camera coordinate system.

## Slide 94: Answers tutorial 2.8
From the question, we can get that
%matlab
rc=[-0.6612 -0.4121 -0.6269
-0.6742 -0.0400 0.7375
-0.3290 0.9103 -0.2513]
c=[1 2 3]'
pw=[5 5 5]'
pa=rc*(pw-c)
Answer: pa =
-5.1349
-1.3418
0.9123

## Slide 95: Tutorial 2.9
Suppose that the intrinsic parameters of our camera can be represented by
The camera coordinate center is the same as the world center, hence Mext =[ I | 0]
There are two points P1, P2 in the world coordinates
  P1 meters , its image is at
  meters, its image is at respectively.
Compute the matrix . (hints : image )

## Slide 96: Answers Tutorial 2.9

## Slide 97: Use ex.2.9 to show how to achieve camera calibration : For a 3D object, assume the camera center is at [0 0 0] meters of the world coordinates. The cube is 1 meter away from the camera along the Z-axis. This model is easy to find if the size of squares are known, say 0.1m2 for each checker element
Set here as
Object orgin,
[0,0,1] meter
what is the 3D/2D positions [Xw,Yw,Zw],[u,v] of this point in cm,pixels resp.?
Answer:
[0.3,0.4,1]meters
Estimate its [u,v] image position
Ans: estimated by inspection as [3000,2200?]
Xw
Yw
Zw
what is the 3D positions [Xw,Yw,Zw],[u,v] of this point in cm, pixels resp.?
Answer:
[0.1,0.2,1]meters
Estimate its [u,v] image position
Ans: estimated by inspection as [1000,2000]
u=4000
v=4000
u,v=1,1
Note: you may use this object to calibrate a camera using the method in this tutorial exercise. You can try it on your camera.

## Slide 98: Exercise/answer 2.9 :Illustration of Camera calibration by a 3D object
[0.1, 0.2,1] meters
Zw
Xw
Yw
Set here as
World origin
[0,0,0]
[0.3,0.4,1] meters
[1000,2000]
[3000,2200]
Image
Camera center
= world center
Assume it is [ 0 0 0 1]T meter away from the object
[0 0 0]T