## Slide 1: Image processing and computer vision
Chapter 6: Histogram equalization
and color models
Week 5

## Slide 2: Overview
What is Histogram equalization?
  Recalculate the picture gray levels to make the distribution more equalized
  Used widely in image editing tools and computer vision algorithms
  Can also be applied to color images
Ref: Intensity transformation :ch3 of Gonzalez ed.3 ch3.2 page 122.
Week 6 begins
Ref: Digital image processing, R.C. González, R.E. Woods edition3. ch3 of Gonzalez ed.3 ch3.2 page 120-128. It can be found at http://books.google.com/

## Slide 3: Why ? :Histogram equalization makes the picture look better.
Eample:Histogram h(rk)=nk
  nk = number of pixels in the image that have grade level rk.
  Since total number of pixels=M*N
  K=0,1,2,..L-1 gray level (up to you, e.g. 8-bit 256 levels; 16-bit 65536 levels)
  A normalized histogram
Bright image
Normalized
Count
(value =01)
P(rk)=nk/MN
Grad level(0-255) rk
N
columns
M rows
Each pixel has
a gray level rk
.
P(rk)

## Slide 4: Example: Normalized histogram
An image of 9 pixels (M=3, N=3)
K=0,1,2,..,L-1=255.
L=256 levels
0 | 250 | 250
100 | 100 | 100
55 | 55 | 10
3/9
2/9
1/9
Normalized
Count
P(rk)=nk/MN
Normalized histogram
0 10 55 100 250
Grade level(0-255) rk
level | count
0 | 1
10 | 1
55 | 2
100 | 3
250 | 2

## Slide 5: CMSC 5711- ch6 Histogram Exercise 1: Normalized histogram
An image of 5x4 pixels (M=?__, N=?___)
K=0,1,2,..,L-1=255.
L=256 levels
Sketch the histogram (??)
1
0.5
Normalized
Count
P(rk)=nk/MN
Normalized histogram (plot it)
0 100 200
Grad level(0-255) rk
7 | 100 | 200 | 45
2 | 100 | 7 | 120
100 | 100 | 7 | 120
200 | 100 | 45 | 100
200 | 200 | 45 | 45
N columns
M
rows
level | count
2 | ?
7 | ?
45 | ?
100 | ?
120 | ?
200 | ?

## Slide 6: Exercise 2 : In each histogram (a) Identify the gray levels that have not been used. (b) Which gray level is the highest?
Bright image
Low contrast image
Histogram1
Pixels are
concentrated
at too high
grade levels
Pixels are
concentrated
at too low
grade levels,
Distribution is
too narrow.
Both images are not ideal: too bright or too dark. To fix it, use histogram equalization
0 50 100 150 200 250 300
Answer:?
Histogram2

## Slide 7: Histogram equalization: Motivation
A mapping s=T(r) is needed, so that Probabilities of all pixel levels in the ‘s’ domain is a constant.
Change the scale from ‘r’ to ‘s’ domain using the mapping s=T(r).
Histogram quantization procedure: E.g. pixels of the gray level rk (say rk=0.75, for pixel levels are normalized from 0 to 1) in the original image may need to be changed to 0.82 in the normalized image.. etc.
So that Ps(sk=0.1)=Ps(sk=0.82)=Ps(sk=0.95)...= Ps(sk=all values)=a_constant. They are the same. But because of digitization, some errors may exit.
Sk
rk
1
1
r
sk=T(rk)
0,0
s
Input gray values
(to be normalized)
Output (normalized) gray values

## Slide 8: Effect of histogram equalization
Input: The picture is poorly shot. Most pixel gray levels are located in a small range.
Output: Use histogram transform to map the pixels in ‘r’ domain to ‘s’ domain . So in the ‘s’ domain, each s gray level has a similar number of pixels.
Input: Low contrast image
Output: High contrast image
S domain
r domain

## Slide 9: Histogram equalization: The main problem is to choose a monotonic increasing relation T(r)
A monotonic increasing
relation is needed
sk=T(rk)
rk
L-1=T(L-1)
L-1
r
T(r)
0
T(r)

## Slide 10: Objective of histogram equalization
We want to find T(r) so that Ps(s) is a flat line.
sk
rk
L-1
L-1
r
T(r)
0
Objective:
To find the
Relation s=T(r)
Pr(r)
r
Ps(s)=a constant
(flat horizontal line)
s
L-1
L-1
L-1
Equalized distribution
Input random distribution
The original image
The probability of these levels are lower)
The probability of these levels are higher
The probability of all levels are the same
In Ps(s)
s=T(r)

## Slide 11: How to find S=T(s)?
Assume we know,
We want to prove that ps(s) is a constant, if the above formula holds.
Later we will show:
if formula (1) is true, ps(s) is a constant

## Slide 12: Exercise 3
A numerical example, fill in the blanks

## Slide 13: Exercise 4: Based on (1) we want to prove ps(s)= constant
(2 slides back)
We want to show: if formula1 is true, Ps(S) is a constant

## Slide 14: Discrete form for practical use
From the continuous form of formula (1) to its discrete form

## Slide 15: How to do the mapping?
Having found the relationship
Transform the original image to obtain a equalized one by the Look-up table T(r).
For (x=0;x<N-1;x++) //For all pixels in the image
{For (y=0;y<M-1;y++) //
{ rk=source_image (x,y);
newImage(x,y) = T(rk); //use the lookup table
}
}
sk
rk
L-1
L-1
r
T(r)
0
Look up table

## Slide 16: Exercise 5
(a) A numerical exercise, fill in the blanks
(b) when rk=source_image(x,y)=4, newimage(x,y) will become ?__.
(c) What is the relation of the variables : Total , M,N and nk?
(d) What is the “histogram back projection" of a pixel having pixel level 2?
(d) What is the “histogram back projection" of a pixel having pixel level 4?

## Slide 17: Histogram equalization
Most pictures are in color, having multiple color channels.
We need to equalize color pictures
Then, how to represent color images?

## Slide 18: Color models
Cartesian-coordinate representation
  RGB (Red , Green , Blue)
Cylindrical-coordinate representation
  HSV (Hue, saturation, value)
  HSL (Hue, saturation, Light)
  etc
HSV
  http://en.wikipedia.org/wiki/HSL_and_HSV#From_HSV
RGB

## Slide 19: From RGB to HSV or HSL
RGB=red, green, blue (Cartesian-coordinate representation) not relevant to our perception)
So change RGB to cylindrical-coordinate representations , there are 3 choices:
  HSV (Hue, saturation, value)
  HSL (Hue, saturation, Light)
  HSI (Hue, saturation, Intensity)

## Slide 20: Hue色調
http://en.wikipedia.org/wiki/Hue
“the degree to which a stimulus can be described as similar to or different from stimuli that are described as red, green, blue, and yellow,”
The same numerical value for ‘Hue’ in HSV and HSL representations of the same picture
Encoded in degree
max=max_value(R,G,B)
min=min_value(R,G,B)
if R = max, H1 = (G-B)/(max-min)
if G = max, H1 = 2 + (B-R)/(max-min)
if B = max, H1 = 4 + (R-G)/(max-min)
H = H1 * 60
Hue

## Slide 21: Cylindrical geometry of Hue (0-360o)
http://en.wikipedia.org/wiki/File:Hsv-hexagons-to-circles.svg
0o
Red
Primary
120o
Green
Primary
240o
Blue
Primary
Mixing
Red/Green
Mixing
Green/Blue
Mixing
Blue/Red
Wrap round

## Slide 22: Lightness亮度: 3 different methods to encode brightness: Intensity (I), Value (V), Light (L)
Given RGBraw (each channel 0-255 levels) pixels of a picture.
Normalize it first , e.g. each channel is 8-bit.
R=Rraw/255; G=Graw/255; B=Braw/255;

## Slide 23: Saturation色彩飽和度
Saturation: “Saturation is the colorfulness of a color relative to its own brightness” from http://en.wikipedia.org/wiki/Colorfulness
Not the same numerical values for HSV and HSL representations of the same picture
HSV
HSL

## Slide 24: Different saturation (s) values (range 0-1)
S=1 =0.75 =0.5 =0.25
More water
Less water

## Slide 25: Saturation Calculation
http://en.wikipedia.org/wiki/HSL_and_HSV
HSL HSV

## Slide 26: Exercise 6: From RGB (3x8-bit) to HSV
Hue (0->
360o)
max= max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)

## Slide 27: Exercise 7
RGB=(18,200,130)
What are the values in HSV,HSL,HSI?
Answer:

## Slide 28: Color histogram equalization
Change the RGB representation to HSV
Do histogram equalization for the V channel.
The other two channels (H,S) remain unchanged.
Put back the equalized HSV image back to RGB

## Slide 29: Programs and demos
Histogram in OpenCV:
  Calculate Histogram: http://opencv.willowgarage.com/documentation/cpp/histograms.html?highlight=calchist#calcHist
  Convert color space:
  http://opencv.willowgarage.com/documentation/cpp/miscellaneous_image_transformations.html?highlight=cvtcolor#cvtColor
  Histogram equalization
  http://opencv.willowgarage.com/documentation/cpp/histograms.html?highlight=equalizehist#equalizeHist

## Slide 30: Programming Exercise
A programming exercise with OpenCV to histogram equalize a color image
  Given an RGB color image, convert it to HSV color space, compute its histogram on the V channel
  Do histogram equalization for the V channel and generate the equalized RGB image.

## Slide 31: Summary
Studied gray level histograms
Learned histogram equalization
Learned color models and equalization of color images

## Slide 32: Reference
Digital image processing, R.C. González, R.E. Woods edition3. ch3 of Gonzalez ed.3 ch3.2 page 120-128. It can be found at http://books.google.com/
http://en.wikipedia.org/wiki/Histogram_equalization

## Slide 33: Appendix

## Slide 34: ANSWER1: Exercise 1: Normalized histogram
An image of 5x4 pixels (M=?__5, N=?___4)
K=0,1,2,..,L-1=255.
L=256 levels
Sketch the histogram
1
0.5
Normalized
Count
P(rk)=nk/MN
Normalized histogram(plot it)
0 100 200
Grad level(0-255) rk
7 | 100 | 200 | 45
2 | 100 | 7 | 120
100 | 100 | 7 | 120
200 | 100 | 45 | 100
200 | 200 | 45 | 45
N columns
M
rows
level | count
2 | 1
7 | 3
45 | 4
100 | 6
120 | 2
200 | 4

## Slide 35: Answer2: Exercise 2 : In each histogram (a) Identify the gray levels that have not been used. (b) Which gray level is the highest?
Bright image
Low contrast image
Histogram1
Pixels are
concentrated
at too high
grade levels
Pixels are
concentrated
at too low
grade levels,
Distribution is
too narrow.
Both images are not ideal: too bright or too dark. To fix it, use histogram equalization
0 50 100 150 200 250 300
Answer:
Histogram 1: 0->130
Histogram 2: 0->90, 140255
(b) Histogram 1, around255. Histogram 2 around 100
Histogram2

## Slide 36: Answer3a: Ex3
A numerical exercise
36

## Slide 37: Answer 3b:Matlab : Exercise 4:
Ma
%ex3
%note index is shifted because matrix cannot have zero index
n(1)= 790
n(2)= 1023
n(3)= 850
n(4)= 656
n(5)= 329
n(6)= 245
n(7)= 122
n(8)= 81
M =64
N =64
L =8
for j=1:L
p(j)=n(j)
temp=0
for k=1:j
temp=n(k)+temp
end
s(j)=((L-1)/(M*N))*temp
end
n
s
Round(s)
s = 1.3501 3.0984 4.5510 5.6721 6.2344 6.6531 6.8616 7.0000
n = 790 1023 850 656 329 245
122 81
s = 1.3501 3.0984 4.5510 5.6721 6.2344 6.6531 6.8616 7.0000
Roudn s=
1 3 5 6 6 7 7 7

## Slide 38: Answer4: Exercise 4: Based on (1) we want to prove ps(s)= constant
Conclusion: if formula (1) is true, ps(s) is a constant
The Second Fundamental Theorem of Calculus
http://www.ltcconline.net/greenl/courses/105/Antiderivatives/secfund.htm

## Slide 39: Answer5: Ex 5
(a) A numerical exercise, fill in the blanks
(b) when rk=source_image(x,y)=4, newimage(x,y) will become ?_6_.
(c) What is the relation of the variables : Total , M,N and nk?
Answer: Total=M*N=Sum of all nk=0,1,..,Total
Answer (d, e) In a certain image, the "histogram back projection of a gray level " means the probability of a pixel having that gray level. So "histogram back projection” is the same as pr (rk). Say, in this image the probability a pixel having pixel level rk=2 is 0.0078 or a pixel having pixel level rk=4 is 0.02393. That means in this image, the "histogram back projection" of a pixel having pixel level 2 is 0.0078 or the "histogram back projection" of a pixel having pixel level 2 is 0.02393.

## Slide 40: Exercise 6: From RGB (3x8-bit) to HSV
max= max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)
Ex6: Find R,G,B values and the color of
each of following cases:
when V=0.5,H=0o,S=1.
when V=0.2,H=120o,S=0.8
when V=0.6,H=260o,S=0.5.
when V=0,H=0o,S=1.
when V=0.5,H=0o,S=1.
H=0-120 120-240 240-260
H1=0-2 2-4 4-6

## Slide 41: Answer 6a,b:Exercise 6: From RGB (3x8-bit) to HSV
max=max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)
6a) when V=0.5,H=0,S=1, the color is :
From (7) max=0.5*255=127.5
From (8) S=(max-min)/max=1,
max-min=max, hence min=0, Since H=0,
the only formula for H1 is (3), because
the other formulas will make H more than 0
From (3) H1 = (G-B)/(max-min)
(G-B)/127.5=0 , so G=B=0
The color is pure red.
----------------------------------------
6b) V=0.2,H=120,S=0.8
H=120 hence H1=2 by formula (6)
From (7) max=0.2*255=51
From (8) S=(max-min)/max=0.8,
max-min=0.8*max, hence min=0.2*max=10.2
Since H1=2, G max be max,
the only formula for H1 is (4), because the other
formulas will make H1 deviate too much from 2
From (4) H1 =2+ (B-R)/(max-min)
2+(B-R)/(51-10.2)=2 , so G=B=0 is the only solution
The color is pure green.
H=0-120 120-240 240-260
H1=0-2 2-4 4-6

## Slide 42: Answer 6c:Exercise 6: From RGB (3x8-bit) to HSV
max=max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)
Hue 0->360o)
6c) when V=0.6,H=260,S=0.5, the color is :
From (eq7) max=0.6*255=153
From (eq8) S=(max-min)/max=0.5,
max-min=0.5*max, hence min=0.5*max=76.5 Since H=260, from (eq6) H1=260/60=4.333,
the only formula for H1 is (eq5), because
the other formulas will make H1 outside 4 to 6
From (eq5) H1 = 4 + (R-G)/(max-min)
4 + (R-G)/(max-min) =4.333
R-G= 0.333*(153-76.5)=25.47
B=max=153,
R-G=25.47, hence R must be bigger than G, hence G=76.5, so R=G+min=76.5+25.47 =101.97
The color (R,G,B)=(153,101.97,76.6)
The color is purple.
----------------------------------------
H=0-120 120-240 240-260
H1=0-2 2-4 4-6

## Slide 43: Answer 6d,e:Exercise 6: From RGB (3x8-bit) to HSV
max=max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)
Hue 0->360o)
6d) when V=0,H=0,S=1,
From (eq7) max=V*255=0*255=0,
so min must be 0. (R,G,B)=(0,0,0)
The color is black.
----------------------------------
6e) when V=1,H=0,S=1,
From (eq7) max=V*255=1*255=255,
H=0, from (eq6) H1=0,
the only formula for H1 is (eq3), because
the other formulas will make H1 outside 0 to 2
From (eq3) H1 =(R-G)/(max-min)
(R-G)/(max-min) =
R-G= 0.333*(153-76.5)=25.47
B=max=153,
R-G=25.47, hence R must be bigger than G, hence G=76.5, so R=G+min=76.5+25.47 =101.97
The color (R,G,B)=(153,101.97,76.6)
The color is purple.
----------------------------------------
H=0-120 120-240 240-260
H1=0-2 2-4 4-6

## Slide 44: Answer 6:Exercise 6: From RGB (3x8-bit) to HSV
max=max_value(R,G,B) ------------------(1)
min=min_value(R,G,B) --------------------(2)
if R = max, H1 = (G-B)/(max-min) -------(3)
if G = max, H1 = 2 + (B-R)/(max-min)---(4)
if B = max, H1 = 4 + (R-G)/(max-min) ---(5)
H = H1 * 60------------------------------------(6)
V=max/255------------------------------------(7)
if H < 0, H = H + 360
s=(max-min)/max---------------------------(8)
Hue (0->
360o)

## Slide 45: Answer7 for ex7
RGB=(18,200,130). Can normalize it first
RGB=(18,200,130)/255.
What are the values in HSV?
Answer:
(for HSV on R=18/255, G=200/255, B=130/255),
max=200/255, m=18/255, since green G=max
H1=2+(B-R)/(max-min), H1=
H1=2+(130-18)/(200-18)=2+(112/182)=2.615, need not to show 255 since they cancel each other in numerator and denominator
H=H1*60=156.9
S=(max-min)/max=(200-18)/200=0.91
V=max/255=0.78
HSL, HSI , see formulas in note