## Slide 1: Image processing and computer vision
Chapter 9: 3D reconstruction and pose estimation from N-frames using Factorization (Structure From Motion SFM) for affine cameras
Week 8

## Slide 2: Methods
Different camera models
  Perspective camera
  Affine cameras
    Orthographic camera
    Weak perspective camera
Factorization (linear/fast, but not too accurate)
  Affine/Orthographic approach
Bundle adjustment (slower but more accurate)

## Slide 3: Relate world 3D to camera 3D coordinates, see 156[1]
Camera motion (rotation=R, translation=C) will cause change of pixel position (x,y)
Pw=World 3D coordinates=[Xw,Yw,Zw]T
Pc=camera 3D coordinates =[Xc,Yc,Zc] T

## Slide 4: Different camera models
  Perspective camera
  No approximation
  Mathematically non-linear , so some people do not prefer it.
Affine cameras
  Approximated cameras (object far away)
  Mathematically linear, good for calculation, e.g
    Orthographic camera
    Weak perspective camera
    Demo program and video

## Slide 5: Exercise 1: Camera and world coordinates
World
coordinates
Camera
coordinates
C
Ycam
Xcam
Zcam
Zw
Xw
Yw

## Slide 6: Perspective Camera: camera motion is R,T
Perspective projection matrix, to make life easier set Kint=I3
Constraint:
Orthogonal matrix:
QT=Q-1
QTQ=QQT=I
If Q is orthogonal

## Slide 7: Perspective Projective
Model M at t=1
c (Image center, ox,oy)
F=focal length
image
Oc=
(0,0,0)
(Camera center)
Xc-axis
Zc-axis
Yc-axis
v-axis
u-axis
X,Y,Z
(u,v)
(0,0) of image plane
Principal axis
Principal
plane

## Slide 8: Some interesting fact
The principal plane is the vector P3 (3th row of P)
Principal plane
Z=0, X,Y can
be values
Camera
center
Image
center
Z Principal
axis
Y
X
At the principal
Plane
Z=0

## Slide 9: Exercise 2: More interesting facts
The principal axis is the vector m3 (3th row of M)
Principal plane
Principal
axis
Camera
center
Image
center
Z
Y
X

## Slide 10: Affine camera model
  Approximated cameras (object far away)
  Mathematically linear, good for calculation, e.g.
    Orthographic camera
    Weak perspective camera

## Slide 11: An affine camera is an approximation of the perspective camera
Recall: Perspective camera matrix
Constraint:
  The 3x3 sub_matrix [p11 to p33] is orthogonal--it is a 3x3 rotation matrix. If Q is an orthogonal matrix:
    QT=Q-1
    QTQ=QQT=1
Affine camera matrix
Last row is [0 0 0 1]
Constraint:
  Rank 2 for [submatrix(P11P23)]
Constraint:
Rank 2

## Slide 12: Exercise 3:From perspective to affine if depth (Z) is large enough, a perspective camera is shown below
C’ is the position of the camera in world coordinates. Imaging the camera is now moving backward along the principal axis -r3 at a rate of (t) pixels per second.
C’ can now be replaced by C-(t)r3, and at t=0, the camera is at C. Note: the principal axis =(r3)3x1, where r3T is the 3rd row of r (proved earlier).

## Slide 13: Exercise 4: Perspective to Affine
In execise3, the object will become smaller and smaller but if we zoom the camera simultaneously by a magnification factor (f f(dt/d0)) the object will maintain the same size on screen, where d0=dt=0.
Magnification matrix

## Slide 14: The proof showed that
When the object is very far away d =dt= 
By definition dt=-r31C+t , r is constant (the rotation is fixed) , C is the initial position of the camera and we view it using a large zoom lens (f f(dt=  /d0)).
The above camera viewing process is an affine viewing process. Note f=focal length.
In reality if the object is far away from the camera, we can approximate it by using the affine camera math model. The advantage is the system is linear and is easier to be handled mathematically by linear algebra.

## Slide 15: Example:Vertigo (film) Hitchcock, 1958 http://www.youtube.com/watch?v=GnpZN2HQ3OQ (around 2:05)
The same set of objects
Perspective Affine
Zoomed out Zoomed in
Object size depends on distance Object size less sensitive to distance
Note the ratio between the floor and hands: Larger
The ratio between the floor and hands: smaller

## Slide 16: Perspective V.s. orthographic
Orthographic camera is an approximated camera model that assumes no depth change
Orthographic camera is a type of affine camera
http://www.soulsofdistortion.nl/images/last_supper.jpg
http://1.bp.blogspot.com/_FOIrYyQawGI/SGLoj58NBiI/AAAAAAAAAoQ/pYvm01Xj8Bg/s1600/LastSupper.jpg

## Slide 17: Affine approximation
Camera focal length =1
t3 =0 (no motion in Z direction, Z is a constant)
Rotation is affine
M2x3, t2x1
Affine rotation, Affine ‘
translation

## Slide 18: Examples of affine cameras
Orthographic camera
Weak perspective camera
both have the same projective matrix form

## Slide 19: Orthographic paintings, sizes of objects do not depend on distances from objects to the viewer
Orthographic, Orthographic
http://www.love-egypt.com/images/painting1.jpg
唐人：宮樂圖
http://www.nigensha.co.jp/kokyu/ch/p01.html

## Slide 20: Other approximated camera models: Weak perspective camera: A type of affine cameras
(Full) Perspective camera image (ui,vi)
  ui=f*Xi / Zi
  vi=f*Yi / Zi
  (ui,vi) depends on Zi
Weak perspective camera image (ui,vi)
  ui=f*Xi / Zmean
  vi=f*Yi / Zmean
  All (ui,vi)s depend on the same depth (Zmean)

## Slide 21: Structure from motion (SFM)
Find the 3D structure/model of an object from a sequence of images taking when the object (or camera) is in motion
We will introduce the method using the Factorization method for affine cameras

## Slide 22: Exercise 5 : Structure from motion for affine cameras a) Discuss differences between the affine and perspective camera. b) Which terms in an affine camera matrix govern affine rotation? c) Which terms in an affine camera matrix govern affine translation?
Input a sequence of image features xj(j=1,..n) of an object, for time i=1,2,…,,.
Find
  Structure of the object, Xj=(X,Y,Z)j for all features points, j=1,2,…N
  camera motion, PAffine for each i

## Slide 23: Tracking (Click picture to see movie)
Demo for
tracking
Demo
http://www.youtube.com/watch?v=RXpX9TJlpd0

## Slide 24: Factorization for Affine Camera P.437[1]

## Slide 25: Factorization for Affine Camera P.437[1]
:

## Slide 26: Motion of the object
3D Model=Xj : where j=feature index =1,2…n features
Time (i)

1 2 3 …
=controid

## Slide 27: Factorization for Affine Camera
Find affine M1,…,M 
Minimization of re-projection error
i = 1,…, (time sample index)
j = 1,…,n (model point index)

## Slide 28: Find translation (t) first: a simple task for affine cameras
At time i, feature index j
For affine cameras translation =[uij, vij]T (size is 2x1)
Centroid is the translation (Centroid =mean of all 2D feature points at time i)

## Slide 29: Exercise 6:
At time i, features are xj
x1=[4, 5]
x2=[6,7]
x3=[1, 8]
Mean is ??_________
The new xj’ is xj’
X1’=?________
x2’=?_________
x3’=?_________
So translation is found
t(x,y)=
?

## Slide 31: Build the measurement matrix W from measurements x’ after translation ti is eliminated
Time index i=1,2,..,
Feature index j=1,2,..,n
x’=[u’,v’]T is an (2x1) image point (translation eliminated).
Time
Index
i=1,2..
Feature index :j=1,2,,n
W=measured 2D image feature (translation eliminated)

## Slide 32: Construct the input data set
We can factorize W to obtain Mi and Xj for all i,j because
Time
Index
i=1,2..
Feature index :j=1,2,,n
Mi
Xi
W=measured 2D image feature (translation eliminated)
Week 9 begins

## Slide 33: Ideal W is Rank 3
From Linear algebra, the rank of a product of A,B is the minimum of { rank (A), rank (B)}.
Both are 3, using linear algebra theory
so the product is rank 3

## Slide 34: Use SVD to set rank 3 constraint to W, (Note solution is not unique, See P438 [1])

## Slide 35: What is SVD? Singular Value Decomposition
A is mxn, decompose it into 3 matrices: U, S, V
U is mxm is an orthogonal matrix
S is mxn (diagonal matrix)
V is nxn is an orthogonal matrix
1, 2, n, are singular values
Columns of vectors of U=left singular vectors
Columns of vectors of V=right singular vectors

## Slide 36: SVD (singular value decomposition)
SVD
Left singular vectors
…
Right singular vectors
Singular values
VT

## Slide 37: %demo the use of svd, khwong
%a=rand(3,4)
a=[1 3 5 7
2 4 6 8
9 10 11 13]
[u,s,v]=svd(a)
disp('a-u*s*v is 0 or very small, see below')
round(a-u*s*v')
a = 1 3 5 7
2 4 6 8
9 10 11 13
u = -0.3428 0.6533 -0.6750
-0.4186 0.5370 0.7324
-0.8410 -0.5337 -0.0894
s = 25.6888 0 0 0
0 3.8837 0 0
0 0 0.0491 0
v = -0.3406 -0.7919 -0.3003 -0.4082
-0.4326 -0.3163 0.2148 0.8165
-0.5246 0.1592 0.7299 -0.4082
-0.6494 0.4974 -0.5752 -0.0000
a-u*s*v is 0 or very small, see below
ans =
0 0 0 0
0 0 0 0
0 0 0 0

## Slide 38: See how SVD can be used here
3 columns
3 rows
VT

## Slide 39: The Factorization Algorithm (part 1)
Measured 2D features (translation eliminated)

## Slide 40: Exercise 7: indicate in the diagram below where are the vectors: U1,U2,U3, v1,v2,v3 that enforce the rank3 constraint
VT
U
VT
U

## Slide 41: The Factorization Algorithm (part 2): Metric upgrade
The M and X obtained previously are only approximations because they do not satisfy the metric transform constraint, that means

## Slide 42
Ref: Morita and Kanade,"A Sequential Factorization Method for Recovering Shape and Motion From Image Streams", IEEE PAMI, VOL. 19, NO. 8, AUGUST 1997

## Slide 43
Ref: Morita and Kanade,"A Sequential Factorization Method for Recovering Shape and Motion From Image Streams", IEEE PAMI, VOL. 19, NO. 8, AUGUST 1997

## Slide 45: Reconstruction result
Structure From Motion -- factorization method demo
--Input: 18 frames
--Output: VRML file
Mat lab implementation
http://www.youtube.com/watch?v=azl-DGK6e1U
Python implementation
https://www.youtube.com/watch?v=TeakxTW20mI
Input
Wireframe output
Model output

## Slide 46: Bundle adjustment
Non linear iterative method is more accurate than linear method, require first guess.
Usually factorization gives the first guess for the bundle adjustment method.

## Slide 47: Summary
Studied the factorization structure-from-motion method for single camera multiple views

## Slide 48: Reference
[1] Hartley and Zisserman, Multiple geometry in computer vision, Cambridge, University Press. 2002.
[2] Morita and Kanade,"A Sequential Factorization Method for Recovering Shape and Motion From Image Streams", IEEE PAMI, VOL. 19, NO. 8, AUGUST 1997

## Slide 49: Appendices

## Slide 50: Appendix 1 More properties of SVD

## Slide 51: Appendix 2 Frobenius norm
A is an m-by-n matrix Frobenius norm ||A||F
See http://mathworld.wolfram.com/FrobeniusNorm.html

## Slide 52: Appendix 3 Rank of matrix http://en.wikipedia.org/wiki/Rank_(linear_algebra)
If A is of size m x n, Rank(A)<min{m,n}
Rank(AB)< min{rank(A), rank(B)}
Rank(A)= number of non zero singular value found using SVD.

## Slide 53
Appendix 4 Different approximate camera models

## Slide 54: Appendix 5

## Slide 55: Answer1: Camera and world coordinates
World
coordinates
Camera
coordinates
C
Ycam
Xcam
Zcam
Zcam
Xcam
Ycam

## Slide 56: Answer2: Exercise 2: More interesting fact
The principal plane is the vector P3 (3th row of P)
Principal plane
Principal
axis
Camera
center
Image
center
Z
Y
X
At the principal
Plane
Z=0

## Slide 57: Answer 3

## Slide 58: Answer 4: Perspective to Affine
Of course the object will become smaller but if we zoom the camera simultaneously by a magnification factor of (dt/d0) the object will maintain the same size on screen.

## Slide 59: Ans:Exercise 5 : Structure from motion for affine cameras a) Discuss differences between the affine and perspective camera. Ans: Affine: last row is [0 0 0 1] b) Which terms in an affine camera matrix govern affine rotation? Ans: m11,m12,m13,m21,m21,m22 c) Which terms in an affine camera matrix govern affine translation? ans:T1 t2
Input a sequence of image features xj(j=1,..n) of an object, for time i=1,2,…,,.
Find
  Structure of the object, Xj=(X,Y,Z)j for all features points, j=1,2,…N
  camera motion, PAffine for each i

## Slide 60: Answer: Exercise 6
At time i, features are xj
x1=[4, 5] T
x2=[6,7] T
x3=[1, 8] T
Mean is
=[(4+6+1)/3, (5+7+8)/3] T=[3.67,6.67]T
The new (translation eliminated) xj is xj’
x1’=[4-3.67,5-6.67] T=[0.33,0.33] T
x2’=[6-3.67,7-6.67] T=[2.33,0.33] T
x3’=[1-3.67,8-6.67] T=[-2,67,1.33] T
So translation is found
t(x,y)=[3.67,6.67] T

## Slide 61: After translation (t) is found Process input features to eliminate translation
At time i, features are xj
x1=[4, 5]
x2=[6,7]
x3=[1, 8]
Mean is [(4+6+1)/3, (5+7+8)/3]=[3.67,6.67]
The new xj is xj’
x1’=[4-3.67,5-6.67]=[0.33,0.33]
x2’=[6-3.67,7-6.67]=[2.33,0.33]
x3’=[1-3.67,8-6.67]=[-2,67,1.33]
So xj’ is now the input (instead of xj)

## Slide 62: Answer7:Exercise: indicate in the lower diagram where are the vectors: u1,u2,u3, v1,v2,v3 Enforce rank3 constraint
3
3
VT
U
v1,
v2,
v3
u1,u2,u3

## Slide 63
>>running result
rank(a) is 4
find svd : [u,s,v]=svd(a)
u=-0.2861 -0.4365 0.3907 0.7582
-0.5835 -0.5352 0.1321 -0.5964
-0.7075 0.6956 0.0888 0.0877
-0.2776 -0.1980 -0.9066 0.2485
s = 20.6985 0 0 0
0 9.6845 0 0
0 0 3.9981 0
0 0 0 1.6733
v = -0.7078 0.6946 -0.0844 -0.0972
-0.2578 -0.3908 -0.0377 -0.8828
-0.4356 -0.4743 -0.6719 0.3658
-0.4928 -0.3739 0.7349 0.2780
a_same =1.0000 2.0000 4.0000 6.0000
5.0000 6.0000 7.0000 8.0000
15.0000 1.0000 3.0000 5.0000
3.0000 2.0000 6.0000 1.0000
a = 1 2 4 6
5 6 7 8
15 1 3 5
3 2 6 1
make it rank3 by setting ss(4,4)=0
ss = 20.6985 0 0 0
0 9.6845 0 0
0 0 3.9981 0
0 0 0 0
using the ss,find aa=u*ss*vT
aa =1.1233 3.1201 3.5359 5.6473
4.9030 5.1190 7.3651 8.2775
15.0143 1.1296 2.9463 4.9592
3.0404 2.3671 5.8479 0.8844
rank(aa), should be 3
%svd_demo1.m
a=[1 2 4 6 ;5 6 7 8;…
15 1 3 5; 3 2 6 1]
'rank(a) is '
rank(a)
'find svd : [u,s,v]=svd(a)'
[u,s,v]=svd(a)
a_same=u*s*v'
a
'make it rank3 by ss(4,4)=0‘
ss=s, ss(4,4)=0
'using the ss,find aa=u*ss*vT'
aa=u*ss*v'
'rank(aa), should be 3'
rank(aa)